PRESS RELEASE

Merebank pilot plant treats both domestic and industrial wastewater

24 August 2016: Hatch was responsible for the process design of an anaerobic digestion pilot plant at eThekwini Water & Sanitation’s Southern Wastewater Treatment Plant in Merebank, Durban. The plant is unique in that it can accommodate both domestic and industrial waste streams.

The high percentage of industrial waste coming in meant that eThekwini required the pilot plant to have two waste trains, from two industrial sewers and one domestic one, explains Hatch Chemical Engineer – Water Wade Swannell.

“The reasoning behind the pilot plant was to test the ideal operating conditions for the digestion of the particular sludge that needs to be processed here, as Merebank differs from traditional domestic wastewater treatment works,” Swannell explains.

In terms of the general process flow, there is a continuous feed into a flow tank. This is pumped proportionally to primary settling tanks so as to simulate the diurnal flow of the sewer. Sludge thickeners process the sludge further, following which it is pumped to digesters. “All the while there is a constant overflow going back to the sewer,” Swannell elaborates.

The main challenge associated with the project has been its small size, with a nominal capacity of 14 m3/hour. “It is difficult to size equipment that small, which is why we opted for a semi-batch process design. Despite being small, we still put in the same design effort as with a larger project, especially as it has quite a complex control system,” Swannell points out.

The pilot plant has already been commissioned, and is currently in the one-year contractor’s defects liability period. “While our technical role is now at completion, we are looking to stay involved from a research-and-development perspective, as we are quite interested in the results that will come out of the pilot plant.”

Swannell highlights that the pilot plant is expected to provide valuable data on the dual treatment of domestic and industrial wastewater, which poses a particular challenge in water-stressed South Africa.

In terms of ongoing projects, Swannell reveals he is project managing a pilot plant at the Darvill Wastewater Treatment Works for Umgeni Water to take final effluent and treat it to potable-water standard. This 2 Ml/day pilot plant is anticipated to set a new benchmark in this regard. Swannell is also involved with a project to treat mine water for supply to a power station in Mpumalanga.

Ends

Notes to the editor
To download hi-res images for this release, please visit http://media.ngage.co.za and click the Hatch link to view the company’s press office.

About Hatch 
Hatch supplies process and business consulting, information technology, engineering, procurement and project and construction management and operational services to the mining, metallurgical, energy and infrastructure industries.

Media Contact
Mmule Ncongwane
NGAGE Public Relations 
Phone: (011) 867-7763
Fax: 086 512 3352
Cell: 083 661 8751
Email: mmule@ngage.co.za 
Web: www.ngage.co.za

Browse the NGAGE Media Zone for more client press releases and photographs at http://media.ngage.co.za