PRESS RELEASE

AECOM completes work on Plankenbrug outfall sewer in Stellenbosch

28 July 2017: As Lead Design Engineer, AECOM carried out construction monitoring of Phase 1 of the Plankenbrug Main Outfall Sewer and Associated Works in Stellenbosch. Construction commenced in October 2015, and was completed in March.

The new Plankenbrug Outfall Sewer replaced the three main outfall sewers servicing Stellenbosch town, from the Distillery Road bridge over the Plankenbrug River near Bosman’s Crossing, to the downstream Stellenbosch Wastewater Treatment Works off Vredenburg Road.

The existing outfall sewers ranged from 375 mm to 625 mm in diameter. An outfall sewer receives sewage from the collecting system, and conveys it to a point of final discharge, or to a disposal plant. “These outfall sewers had reached the end of their design lives, and a new outfall sewer was required urgently to provide additional flow capacity to the expanding Stellenbosch town,” AECOM Engineer Christian Jordaan commented.

The new outfall sewer has a total length of 1 815 m, which is made up of 45 m of 1-m-diameter and 1 770 m of 1.2-m-diameter pipeline. A length of 240 m was installed by means of pipe jacking underneath a foothill of Papegaaiberg. This avoided open-cut excavation to depths exceeding 10 m, thereby limiting disruption to the area and lowering construction costs.

Using this method, the new outfall sewer was installed underneath a section of the Stellenbosch cemetery, containing a number of large trees, all which remained intact. The pipe jacking was carried out in three sections, which required the construction of three jacking pits. These pits, with a 6 m diameter, were constructed to depths of 5.6 m to 11.8 m.

Installation of the new outfall sewer included construction of manhole structures at roughly 90 m intervals, at lateral tie-in positions, and at changes to the outfall sewer alignment, to allow access for operation and maintenance.

Due to the limited vertical fall available between the upstream and downstream ends of the new outfall sewer, the outfall sewer had to be installed at depths that resulted in clashes with the existing outfall sewers wherever the outfall sewers crossed.

Specially-designed manholes were constructed at these locations, over the existing outfall sewer. The existing outfall sewer penetrated through the new manhole, and hence could remain ‘live’, without discharging into the manhole, until final connection to the new outfall sewer was made.

The manholes typically comprised an on-site cast concrete chamber (with benching) constructed below ground level, with an access chimney. Where depth allowed, working space within the manholes was optimised with the used of 1.8-m-diameter precast concrete rings as the access chimney.

An important aspect of the contract was the communication and liaison with the local community in terms of traffic accommodation, access to residences, security, noise, and dust. Temporary, or partial, road closures were managed continuously. In this regard, a Traffic Accommodation Plan was implemented as part of the contract.

An Environmental Management Programme was also implemented, which contained the procedures and requirements for the protection of the natural environment during construction of the new Plankenbrug Outfall Sewer.

“The project was completed on schedule, and within budget,” Jordaan confirms. “AECOM’s successful partnership with Stellenbosch Municipality and the JVZ Construction & Vakala Construction Joint Venture delivered a service that will accommodate all future developments efficiently, as estimated in the Stellenbosch Sewer Masterplan,” he concludes.

Ends

Notes to the editor
To download hi-res images for this release, please visit http://media.ngage.co.za and click on the AECOM link to view the company’s press office.

About AECOM
AECOM is built to deliver a better world. We design, build, finance and operate infrastructure assets for governments, businesses and organisations in more than 150 countries. As a fully integrated firm, we connect knowledge and experience across our global network of experts to help clients solve their most complex challenges. From high-performance buildings and infrastructure, to resilient communities and environments, to stable and secure nations, our work is transformative, differentiated and vital. A Fortune 500 firm, AECOM had revenue of approximately $18 billion during fiscal year 2015. See how we deliver what others can only imagine at aecom.com and @AECOM.

Media Contact
Mmule Ncongwane
NGAGE Public Relations 
Phone: (011) 867-7763
Fax: 086 512 3352
Cell: 083 661 8751
Email: mmule@ngage.co.za 
Web: www.ngage.co.za

Browse the NGAGE Media Zone for more client press releases and photographs at http://media.ngage.co.za