PRESS RELEASE

SANY hydraulic excavator takes on the toughest working conditions

6 October 2017: Goscor Earth Moving (GEM), part of the Goscor Group, is continuing its introduction of the latest SANY equipment into the local market with the launch of a new hydraulic excavator for the toughest African operating conditions.

The SY215C hydraulic excavator is one of five models developed specifically by SANY for the international market, GEM Sales Director Andre Steenkamp explains. It is equipped with a Mitsubishi 6D34TL engine.

The positive flow controlled hydraulic system means that the main pump’s displacement is directly proportional to the signal pressure from the operator’s joystick. This means that the controller determines the real-time flow demand and variation trend of the actuator, in addition to regulating the displacement.

With a 0.93 m3 bucket capacity, a ground pressure of 47 kPa, an operating weight of 22 200 kg, and 2 000 rpm, the SY215C hydraulic excavator has been developed and designed to perform in the toughest working conditions.

An X-beam design, based on a box-section structure with high strength and durability, provides excellent torsion- and bending-resistance. The track rollers, carrier rollers, and idlers all use seal-in lubrication for improved longevity. The triple grouser track shoes, rolled with a high-strength alloy, provide for excellent contact, stability, and durability.

The track links feature additional reinforced ribs for increased strength and shock absorption when travelling over rough surfaces. A highlight of the SY215C hydraulic excavator is a totally redesigned boom and arm structure that minimises stress points. Comfort and operator safety are also key, in addition to simplified maintenance and service to reduce time and costs, allowing for the lowest total cost of ownership for end users.

Part of the Goscor Group, GEM offers SANY excavators, motor graders, and rollers for the construction, mining, agriculture, sand and stone, forestry, roadworks, and plant hire sectors. The main differentiator for SANY in the local market is highly-competitive pricing for a world-class product, supplemented by increased parts-holding and full in-field service and technical back-up through GEM’s national branch structure, Managing Director Barry Owen comments.

In addition, SANY equipment has been engineered specifically for African operating conditions, including features such as shorter sticks and stronger booms on its excavators for enhanced durability. Major benefits for customers are fuel savings, efficiency, user-friendly design, and reliability.

Ends

Notes to the Editor
To download hi-res images for this release, please visit http://media.ngage.co.za and click the Goscor Group link to view the company’s press office.

About the Goscor Group

Industrial equipment group Goscor is part of Industrial Services Holdings (InServe). Goscor represents leading equipment brands across several sectors. These include Crown, Doosan, Bendi, Hubtex and Taylor Dunn (forklifts and materials handling equipment); Bobcat (compact & construction); SANY (earthmoving); Tennant, Elgin, Maer, Delfin, Kaivac and HighPoint (industrial cleaning equipment); HPower, Weima, Meiwa and Rato (industrial power solutions); Genie (aerial lift equipment); Sullair and Ozen (compressed air solutions), and many more.

Goscor Group Contact
Debby Marx
Group Marketing Communications Manager 
Phone: (011) 230-2600
Fax: (011) 393 5512
Cell: 084 200 2278
Email: dmarx@goscor.co.za
Web: www.goscor.co.za

Media Contact

Jonathan Ducie

NGAGE Public Relations

Phone: (011) 867 7763

Fax: 086 512 3352

Cell: 084 709 0167

Email: jonathan@ngage.co.za

Web: www.ngage.co.za

Browse the NGAGE Media Zone for more client press releases and photographs at http://media.ngage.co.za