PRESS RELEASE

Stabila LAX 50 G is the latest-generation cross-line laser

(Date) 2018: The LAX 50 G self-levelling cross-line laser from Stabila, featuring GreenBEAM technology for optimum visibility, has been launched locally by official African distributor Upat.

The GreanBEAM green laser lines – one horizontal and one vertical line forming a sharp laser cross –  is four times more visibile than red lasers, Upat National Product Specialist Charl Weber notes. These razor-sharp cross-lines are suitable for larger working areas due to their brightness and clarity. The LAX 50 G represents the latest generation of energy-saving laser diodes, which provides for an extended operating time of up to seven hours.

The long, fine laser lines ensure a levelling accuracy of about 0.5 mm for distances of up to 30 m, with laser wave lengths of between 510 nm and 530 nm.

The Stabila LAX 50 G laser is cost-effective, particularly for craftsmen working on interior construction projects. Applications include drywall construction, such as suspending ceilings, positioning interior, partitioning walls, fitting U-profiles, and transferring layouts from the floor to the ceiling.

For electrical installation work, it is ideal for fitting and aligning electrical installations. The Stabila LAX 50 G can also be used for tiling work to mark out tile layouts. The laser is ideal for window-fitting applications, such as levelling window heights. The laser is an excellent tool for joinery applications including kitchen cupboards and aligning worktops.

The Stabila LAX 50 G has been designed specifically for use on construction sites due to its inbuilt pendulum technology, which protects the unit during transport, while a belt pouch ensures easy transport and safe storage.

A circular vial is used to pre-align the laser within a self-levelling range of about 4.5°. The laser can be positioned flexibly and variably to meet the requirements of the specific application. An integrated clamping device on the rear of the unit allows it to be fastened easily to pipes up to 30 mm in diameter.

Weber remarks that a perfect accompaniment to the unit comes in the form of a rotating multi-purpose platform, which allows for the flexible use of the laser both on the floor as well as on camera and construction tripods. Equipped with a strong rare-earth magnet system, the platform is also used to position the unit on metal objects such as U-profiles. The platform also features a hanging hole to attach the laser directly to the wall.

The Stabila LAX 50 G is IP 53-rated for protection against dust deposits inside and against spray (up to 60° on the vertical plane). It is available in a set comprising the laser unit, multi-purpose platform, belt pouch, and three AA 1.5 V batteries. A tripod and LT 30 telescopic laser support are available as options to extend the unit’s application range.

Ends

Connect with Stabila Tools South Africa on Social Media to receive the company’s latest news

Facebook: https://www.facebook.com/STABILAToolsZA/

Notes to the Editor
To download hi-res images for this release, please visit http://media.ngage.co.za and click the Upat link to view the company’s press office.

About Upat
Upat SA (Pty) Ltd. is a 100% South African owned business that began trading in 1983. From the outset, Upat has been committed to the building industry, supplying not only a range of anchor bolts, but also rotary hammer drilling machines, tungsten-tipped masonry drill bits, powder actuated tools, and allied building and construction products. Upat’s ability to supply a range of top-quality products at market-related prices has resulted in it becoming a market leader in Southern Africa. Upat is proudly the sole Southern African distributor of the fischer range of construction fasteners, the Milwaukee power-tool brand and the Stabila range of measuring tools.

Media Contact

Jonathan Ducie

NGAGE Public Relations

Phone: (011) 867 7763

Fax: 086 512 3352

Cell: 084 709 0167

Email: jonathan@ngage.co.za

Web: www.ngage.co.za

Browse the NGAGE Media Zone for more client press releases and photographs at http://media.ngage.co.za