PRESS RELEASE

3-in-1 electronic measuring tool offers a new angle on productivity

(11/06/)2018: Digital electronic angle finding, spirit levelling, and bevel gauging can now all be carried out simply and accurately with a single tool. This is thanks to the three-in-one Stabila TECH 700 DA, distributed exclusively by leading local supplier Upat.

The Stabila TECH 700 DA measures and transfers interior and exterior angles from 0° to 270°. The digital display with large digits, and back-lighting that can be dimmed accordingly, ensures optimum readability, even in poor lighting conditions. Two particularly wide contact edges ensure that angles can be marked reliably in all positions, Upat National Product Specialist Charl Weber explains.

The ‘lock’ function allows operators to use the angle finder as a handy bevel gauge. The tool's design also means it is ideal as a spirit level, as its horizontal and vertical vials can be viewed easily, even when the arm is folded in. An electronic module means that the angle measurements required for a wide array of daily construction activities can be carried out conveniently and quickly.

The ‘ref’ function accepts and saves reference angles, and transfers these to other components. The ‘hold’ function saves the measured values, thereby guaranteeing accurate measurements and quick transfer, even in hard-to-see places. The angle bisectors can also be displayed at the touch of a button, which makes it ideal for quick and accurate miter cuts.

The electronic angle measurement function delivers precise measuring results with an accuracy of about 0.1°, with the module switching off automatically if not used for 60 minutes. The electronic module is IP 54-rated for protection against dust deposits and water spray.

Furthermore, the high-quality Stabila vials enable components to be aligned accurately. Vial-installation technology ensures long-term accuracy when measuring. Measuring accuracy in a normal position is ± 0.5 mm/m, and ± 0.75 mm/m in reverse position.

The high-quality aluminium rectangular profile with reinforcing ribs ensures high stability and a secure grip, while providing for accurate measurements even under the most demanding conditions. Additionally, the tool’s coated measuring surfaces adds to its rugged durability. The Stabila TECH 700 DA is available in two lengths, namely 45 cm and 80 cm, with both including a bag for safe transport and storage on construction sites, in workshops, or in vehicles.

Ends

Connect with Stabila Tools South Africa on Social Media to receive the company’s latest news

Facebook: https://www.facebook.com/STABILAToolsZA/

Notes to the Editor
To download hi-res images for this release, please visit http://media.ngage.co.za and click the Upat link to view the company’s press office.

About Upat
Upat SA (Pty) Ltd. is a 100% South African owned business that began trading in 1983. From the outset, Upat has been committed to the building industry, supplying not only a range of anchor bolts, but also rotary hammer drilling machines, tungsten-tipped masonry drill bits, powder actuated tools, and allied building and construction products. Upat’s ability to supply a range of top-quality products at market-related prices has resulted in it becoming a market leader in Southern Africa. Upat is proudly the sole Southern African distributor of the fischer range of construction fasteners, the Milwaukee power-tool brand and the Stabila range of measuring tools.

Upat Contact

Alison Thomet

Marketing Manager

Phone: (011) 624 67oo

Cell: 082 452 3437

Email: alison.thomet@upat.co.za

Web: www.upat.co.za

Media Contact

Jonathan Ducie

NGAGE Public Relations

Phone: (011) 867 7763

Fax: 086 512 3352

Cell: 084 709 0167

Email: jonathan@ngage.co.za

Web: www.ngage.co.za

Browse the NGAGE Media Zone for more client press releases and photographs at http://media.ngage.co.za