PRESS RELEASE

Best-in-class impact wrench from Milwaukee makes a big impact

26 June 2018: The M18 FUEL™ high-torque impact wrench with friction ring has been engineered by Milwaukee for use by the most demanding tradesmen in the world. It is distributed locally by leading supplier Upat.

The M18 ONE FHIWF34 FUEL™ impact wrench with ONE-KEY™ is the most powerful cordless impact wrench in its class, delivering up 1 627 Nm of fastening torque. Its compact size of 213 mm provides for even greater access in confined spaces.

The M18 ONE FHIWF34 FUEL™ impact wrench comes standard with ONE-KEY™ technology. The ONE-KEY™ app is a digital platform for tools and equipment that allows users to customise, track, and manage their power tools. The added benefit is that ONE KEY™ allows for the tool to be set up for specific applications. The app, a free-to-use inventory management program, is available for download for iOS and Android devices.

Milwaukee Product Specialist Werner Koch adds that the tool’s POWERSTATE™ brushless motor outperforms competitors due to its constant power output. The REDLITHIUM™ M18 B5 battery pack delivers more work per charge, and more work over pack life than any other battery. An onboard REDLINK PC board monitors each cell for load and temperature, meaning less downtime and a longer tool life.

Milwaukee’s proprietary four-mode DRIVE CONTROL™ feature allows users to shift into four different speed and torque settings to maximise application versatility. These settings can also be customised using the ONE KEY™ app. REDLINK PLUS also ensures maximum performance and protection from overload, overheating, and over-discharge.

The tool’s Mode 4 bolt removal function, provides for a maximum nut-busting torque of 2 034 Nm and then shifts to 750 rpm, after the bolt is loosened, thereby ensuring unmatched control when removing fasteners. Additionally, Koch points out that the M18 ONE FHIWF34 FUEL impact wrenches’ integrated blow counting sensor enhances the consistent repeatability of the chosen torque setting.

“This 18 V RED lithium-ion high-torque impact wrench offers quick, tool-free socket changes, with a 3/4 inch friction ring anvil, providing for added operator comfort levels during extended use owing to its contoured soft grip,” Koch concludes.

Ends

Connect with Milwaukee South Africa on Social Media to receive the company’s latest news
Facebook: https://www.facebook.com/MilwaukeeToolZA/

Notes to the Editor
To download hi-res images for this release, please visit http://media.ngage.co.za and click the Milwaukee link to view the company’s press office.

About Upat
Upat SA (Pty) Ltd. is a 100% South African owned business that began trading in 1983. From the outset, Upat has been committed to the building industry, supplying not only a range of anchor bolts, but also rotary hammer drilling machines, tungsten-tipped masonry drill bits, powder actuated tools, and allied building and construction products. Upat’s ability to supply a range of top-quality products at market-related prices has resulted in it becoming a market leader in Southern Africa. Upat is proudly the sole Southern African distributor of the fischer range of construction fasteners, the Milwaukee power tool brand and the Stabila range of measuring tools.

Upat Contact

Jaycee Venables

Marketing Coordinator

Phone: (011) 624 6725

Cell: 079 529 9898

Email: jayceev@upat.co.za

Web: www.upat.co.za

Media Contact

Jonathan Ducie

NGAGE Public Relations

Phone: (011) 867 7763

Fax: 086 512 3352

Cell: 084 709 0167

Email: jonathan@ngage.co.za

Web: www.ngage.co.za

Browse the NGAGE Media Zone for more client press releases and photographs at http://media.ngage.co.za