PRESS RELEASE

fischer launches its most versatile frame-fixing solution to date

16 April 2019: A long expansion element with up to three anchorage depths means that the SXRL range is the most versatile frame-fixing solution to date available from fischer, distributed locally by Upat.

Available in 8mm, 10mm, and 14mm diameters, and anchor lengths reaching up to 360mm, the fischer SXRL frame-fixing solution features anchorage depths in accordance with European Technical Assessment (ETA) requirements, namely 50mm, 70mm, and 90mm for the SXRL 8 and 10mm, 70mm, and 90mm for the SXRL 14.

Upat Technical Manager Kevin Owen highlights that the ‘L’ in SXRL refers specifically to length, with the main feature of this latest nylon plug being that it is about 20mm longer than its predecessor. “The longer an anchor is, the more embedded it is in materials such as concrete, and hence the stronger the fixing.”

A key feature of the SXRL is versatility whereby it is suitable for use in both solid and hollow building materials. The new innovative frame fixing can also be used in a variety of applications including façades, windows, gates and doors, wardrobes, kitchen hanging cabinets, beams, metal brackets, and cable ducts and trays.

The long ribs prevent the nylon plug from turning during installation, ensuring additional safety, especially when set deep. The special geometry of the plug has a v-shaped surface that distributes the loads evenly in the drill hole. This allows for better usability in all building materials, and excellent load values.

An anchorage depth of 50mm is specified for concrete, solid, and hollow building materials for the SXRL 8 and SXRL 10; and an anchorage depth of 70mm in all other building materials. An anchorage depth of 90mm is recommended for hollow building materials and aircrete when using the SXRL 8 and SXRL 14; and, specifically, in aircrete for the SXRL 10.

“The fischer SXRL frame-fixing solution can accommodate substantially higher loads than its predecessor. This higher load capacity depends of course, on the diameter of the anchor selected, the depth and the type of material,” Owen concludes. Upat offers full customer service and technical back-up (given the safety-critical nature of anchors in construction) for any queries regarding correct application and product specification.

Ends

Connect with fischer on Social Media to receive the company’s latest news
Facebook:  https://www.facebook.com/fischerFixingsSA/

LinkedIn: https://www.linkedin.com/company/fischer-fixings-sa/

Notes to the Editor
To download hi-res images for this release, please visit http://media.ngage.co.za and click the Upat link to view the company’s press office.

About Upat
Upat SA (Pty) Ltd. is a 100% South African owned business that began trading in 1983. From the outset, Upat has been committed to the building industry, supplying not only a range of anchor bolts, but also rotary hammer drilling machines, tungsten-tipped masonry drill bits, powder actuated tools, and allied building and construction products. Upat’s ability to supply a range of top-quality products at market-related prices has resulted in it becoming a market leader in Southern Africa. Upat is proudly the sole Southern African distributor of the fischer range of construction fasteners, the Milwaukee power-tool brand, the AEG power-tool brand and the Stabila range of measuring tools.

Upat Contact

Alison Thomet

Marketing Manager

Phone: (011) 624 6700

Cell: 082 452 3437

Email: alison.thomet@upat.co.za

Web: www.upat.co.za

Media Contact

Ilan Solomons

NGAGE Public Relations

Phone: (011) 867 7763

Fax: 086 512 3352

Cell: 072 299 0535

Email: ilan@ngage.co.za

Web: www.ngage.co.za

Browse the NGAGE Media Zone for more client press releases and photographs at http://media.ngage.co.za