PRESS RELEASE

Lovato ATL500 from EM is a simple, easy-to-use ATS solution

17 July 2020: The Lovato ATL500 ready-to-use Automatic Transfer Switch (ATS) is available from leading supplier ElectroMechanica (EM) for automatic or manual switching of the load from a main or primary line to a standby or secondary emergency line and vice versa. It is ideal for panel builders and board manufacturers, genset suppliers and system integrators with applications requiring management of two power sources.

A main feature of the Lovato ATL500 is its self-seeking power supply, which means automatic selection of the best available line for auxiliary power supply (110-240VAC L-N). Transfer between the different lines is managed by contactors and motorised changeovers. It monitors three-phase voltage inputs from two sources and only connects to the output line that is within the limits.

Controller LED indication provides for a simple and clear visualisation of the status of the overall ATS system. Automatic or manual operating mode is selected by means of controller push buttons that also command the manual switching of the load in position I (line 1), 0 (neutral, load not supplied) or position II (line 2), which means there is no need to program any setting on the controller whatsoever.

The Lovato ATL500 comes with built-in NFC connectivity for programming via Android smart devices, both tablets and smartphones, via the Lovato NFC App. This innovative app does not require any connection cable and even operates if the controller has no power supply. The app allows the following to be configured accurately and quickly:

- System parameters: Rated system voltage, rated frequency, type of wiring, voltage control mode

- Password protection for access to the settings

- Changeover settings: Priority line selection, interlock times, feedback delays, etc.

- Protection thresholds and tripping delays: minimum/maximum voltage, minimum/maximum frequency, phase sequence, asymmetry, etc.

- Functioning of the programmable digital inputs and outputs

- Functioning of the potentiometers

- Alarm properties

For each line, the Lovato ATL500 monitors the status of the voltage and the frequency to detect if the line is available and that all the parameters are within the correct limits. The ATL500 completes the range of ATS controllers available from Lovato by means of a basic solution for customers who need a simple and easy-to-use device.

Ends

Notes to the Editor

To download hi-res images for this release, please visit http://media.ngage.co.za and click the ElectroMechanica link to view the company’s press office.

About ElectroMechanica
ElectroMechanica was established in 1984 by David van den Berg as a specialised direct importer and wholesale distributor of high-end industrial electrical products, motor control switchgear and electronic automation products. A wholly-owned South African company, ElectroMechanica offers its clients state-of-the-art products, sourced from leading local and international brands, all complying with recognised international safety standards and performance specifications.

ElectroMechanica Contact

Karen Zotter

Phone: (011) 249 5000

Fax: (011) 496 2779

Email: karenz@em.co.za

Web: www.em.co.za

Media Contact

Thapelo Phukuje

NGAGE Public Relations

Phone: (011) 867 7763

Fax: 086 512 3352

Cell: 079 425 4914

Email: thapelo@ngage.co.za

Web: www.ngage.co.za

Browse the NGAGE Media Zone for more client press releases and photographs at http://media.ngage.co.za