PRESS RELEASE

The ideal structural bonding adhesive for demanding applications

Pratley SP020® Special Performance Industrial Adhesive

30 November 2020: Pratley SP020® is a sophisticated third-generation acrylic adhesive suited for demanding industrial, aerospace and assembly applications.  “Pratley SP020® is the ideal replacement for spot welds and rivets,” highlights Pratley Adhesives Marketing Manager Mark Bell.

Pratley SP020® will bond nearly all metals, ceramics, most thermoplastics, most thermoset plastics and most plastic composites like fibreglass polyester composites. Typical application sectors include automotive, where Pratley SP020® can be used to join thermoplastic assemblies like bumpers and dashboards. It can also join steel or aluminium truck body skins to the ‘top hat’ section stiffeners without stress-raising rivets or welds.

In the electronics sector, Pratley SP020® can fix magnets to loudspeakers and motors. With boat and model aircraft building, it speeds up fibreglass and aluminium component assembly and simplifies production. Some other typical applications include:

- Precision assembly of sheet metal or sheet aluminium

- Assemble signboards

- Assemble panels and reinforcement frames

- Replace spot welding with bonded bead line

- Replace riveted parts with bonded bead line

- Assemble fibreglass boat parts

Special performance properties of Pratley SP020® include high peel strength, fast cure, toughness, choice between ‘mix’ and ‘no mix’ application, impact resistance, bonds most plastics, no primer required, bonds oily surfaces, easy application on production lines, exceptional oil and paraffin resistance and extremely tolerant of malproportioning.

Before applying Pratley SP020®, clean the surface by lightly abrading or scouring to remove any dust and rust. Removal of any oil is not necessary but does improve the bond strength. For the ‘mix’ method, squeeze out equal quantities from each tube onto one surface and mix with a spatula. This method is suitable if less than 4 g of adhesive is used.

Alternatively, for the ‘no mix’ method, place a blob or bead of Part A onto one surface and an equal sized blob or bead of Part B onto the other surface, taking care not to smear it. This method is recommended if quantities over 4 g are used, which give off excessive heat if mixed.

Bring the surfaces together with a sliding action to mix and spread the adhesive, which can be done within two minutes when using the ‘mix’ method. Adjust the substrates to the desired position and apply pressure with weights or clamps. “Applying the ‘mix’ method will generally improve strength. However, it is often much more convenient to apply the ‘no-mix’ method especially in a production environment,” concludes Bell.

Connect with Pratley on Social Media to receive the company’s latest news

Facebook: https://www.facebook.com/PratleySA/

Twitter: https://twitter.com/PratleySA

Ends

Notes to the editor

To download hi-res images for this release, please visit http://media.ngage.co.za and click on the Pratley Group link to view the company’s press office.

About Pratley
Established in 1948 by George ‘Monty’ Pratley, the various   companies in the Pratley stable rest on a foundation of research and innovation in both the manufacturing and mining sectors. The various Pratley companies, drawing from 70 years of experience, have filed over 350 patents worldwide, and are ISO 9001 certified. Operating divisions are Pratley Adhesives, Pratley Electrical, Pratley Analytical, Pratley Perlite & Zeolite Mining, Pratley Craft & Decoupage, Select Hairdressing Supplies.

Pratley Contact

Sales

Phone: (011) 955 2190

Fax: (011) 955 3918

Email: sales@pratley.co.za

Web: www.pratleyadhesives.com

Media Contact
Renay Tandy
NGAGE Public Relations 
Phone: (011) 867-7763
Fax: 086 512 3352
Cell: 082 562 5088
Email: renay@ngage.co.za 
Web: www.ngage.co.za

Browse the NGAGE Media Zone for more client press releases and photographs at http://media.ngage.co.za